04.06.2020 Г., группа 2 МСХ

Урок 75-76

Тема урока: Топливная система.

Прочитайте и устно переведите текст.

Письменно выполните упражнения 1 и 2 после текста и отправьте на электронный адрес achmiz2015bachmiz@mail.ru

Отправляя задание, обязательно укажите фамилию, группу, дату и номер урока.

Текст Fuel System

The fuel system is designed to store liquid gasoline and to deliver it to the engine cylinders on the intake stroke in the form of vapor mixed with air. The fuel system must vary the proportions of air and gasoline vapor to meet the requirements of the various operating conditions. Thus for initial starting with a cold engine a very rich mixture of about 9 pounds of air to 1 pound of gasoline is needed. After the engine has warmed up, it will run satisfactorily on a leaner mixture of about 15 pounds of air for each pound of gasoline. For ensuring acceleration and full load or high speed operation, the mixture must again be enriched.

The fuel system consist of a tank in which the liquid gasoline is stored, a fuel line, or tube, through which the gasoline can be brought from the tank to the engine, a pump, which pulls the gasoline through the fuel line, and a carburetor, which mixes the gasoline with air. The carburetor is designed to mix each pound of gasoline with 9 to 15 pounds of air under various operating conditions. The richer mixtures of about 9 pound of air per pound of gasoline are for starting, initial warm-up, and acceleration, while the leaner mixtures of about 15 pounds of air per pound of gasoline are for normal over-the road operation.

Упражнения:

- Переведите на русский язык следующие слова и словосочетания:

The fuel System, store liquid gasoline, engine cylinders, vapor mixed, initial starting, acceleration, or tube, pulls the gasoline, the carburetor is designed

2. Закончите предложения, выбрав их из текста

- The fuel System is designed…

- After the engine has warmed up, it will run satisfactorily on a leaner mixture of about...

- The fuel system consists of a tank in which…

- The carburetor is designed to mix each pound of gasoline